Device Driver
Introduction :
This document describes the device driver which has been injected in the iSense-V4 kernel. We shal have a broad description of the injected devices later. Let’s discuss about the device driver concept. A device driver is a software program that controlls a perticular type of external peripheral hardware (device) connected to the CPU. While loading any OS to the system, some basic device drivers are built into the product. However if a user buys a new type of device that the operating system did not anticipate, a new device driver has to be injected which will handle the new device smoothly. A device driver essentially allows smooth communication between a connected hardware device and the OS. In linux OS, all the devices are available at path /dev .

Injected device drivers :
1. MODEM :-
We have developed a device called “modem” as a kernel module which has been placed in the path /dev/. We have already discussed the objective of a device-driver. Now let’s discuss the modem device-driver in details.

The iSense-V4 communicates to the cloud through various external devices. The modem is one of those. We have used the Quectel-EC25 modem which supports LTE band. The purpose of the device /dev/modem is to create a tunnel between the kernel space and user space. Which enables a smooth and uninterrrupted flow of data inbetween the user and kernel space. Apparrt from that, It properly enables and disables the modem in critical conditions and in bootup time. The device follows thread safety mechanism and also has the ability to handle the dead-lock situations efficiently. This will reduce the development time of the user application, because the user does not need to care about the multi-thread and multi process access to the device separately. As the LTE modems are very sensitive, We have made the device signal free. That meanse, no controll signals (^C, ^Z etc. ) from the user space can not interfair with the modem operation.

Note :
The signal free operation has it’s own advantages and disadvantages. Therefore we are currently performing some experiments on it. If this feature does interfaire with the interrupts, then we may remove this.

How to use it :
In boot-up time, the device will enable the modem. The following table explaines the device usage.

Note : Currently the device Supports only Quectel modem. The device /dev/modem only accept characters.